## Slide 1: CS 419: Production Rendering Introduction to Monte Carlo Methods
Eric Shaffer

## Slide 2: The Power of Randomization
Randomization is an important tool in algorithm design.
Las Vegas algorithm: uses randomness but always yields same result for same input
Monte Carlo algorithm: give different results depending on “random” inputs used…give right answer on average

## Slide 3: Expected Value and Variance

## Slide 4: Estimated E[x]

## Slide 5: Law of Large Numbers
As the number of samples goes to infinity, the error goes to zero and the answer converges to the correct number

## Slide 6: Continuous Versions

## Slide 7: 2D Example…computing π

## Slide 8: 2D Example…computing π

## Slide 9: 2D Example…computing π

## Slide 10: 1D Example
Monte Carlo estimator for integral I

## Slide 11: Central Limit Theorem
If you are sampling an average, the distribution of the average approaches the normal distribution, even if the the distribution being sampled from is not normal
As N approaches infinity, the estimate lies in a narrower band around the expected value of the integral with higher probability
Within three standard deviations 99.7% of the time
Standard deviations vary as 1/√N

## Slide 12: Larger N Reduces Variance

## Slide 13: Variance Reduction
Variance V=σ2
Based on what we’ve seen, if we wanted to cut error in an N sample estimate in half how many samples would we need to take?
Monte Carlo methods converge slowly
  But often are the only realistic option
Variance reduction techniques can help

## Slide 14: Importance Sampling
Do not sample uniformly
Sample with a density that has a similar shape to the shape of f(x)

## Slide 15: Summary: Monte Carlo Integration
Computing the expected value of a function is an integral
We can estimate expected value using random sampling
  By the Law of Large Numbers
  So…we can estimate an integral by sampling
Each integral estimate is an average
These averages form a normal distribution
  By the Central Limit Theorem
The estimate will fall within 1 standard dev. with high probability
  Can reduce the standard deviation by using more samples in the avg.
  Error reduction behaves like the function

## Slide 16: Stochastic Simulation with MC
Two requirements for Monte Carlo
  Know which probability distribution you need to sample
  Generate sufficiently random numbers
Random Numbers
  Most Random Number Generators (RNGs) are pseudo-random
    Any idea why?
  You can get faster convergence with a quasi-random sequence
    Doesn’t clump, samples more or less uniform across domain
      Hammersley and Halton are examples
    Why not just use a uniform grid of samples?